## Slide 1: Wall Tetris Project
Supervisor: Boaz Mizrachi
Presented by: Mohammad Sarris, Yanal Gawanma winter 2024

## Slide 2
Project Motivation
  learning about embedded systems.
  Combining Software and Hardware Skills.
  Learning Advanced Communication Protocols.
  Addressing Technical Challenges.

## Slide 3
Project Goals
  Develop a Functional Tetris Game.
  Integrate Android App with ESP32.
  Design and Assemble a 20x40 LED Matrix.
  Ensure Real-time Communication.
  Implement Score Tracking and Display.
  Overcome Technical Challenges.

## Slide 4
Final Physical layout
20 LED’s Per Row
40 Rows
40 * 20 = 800 LEDs
Connected the LED strips like a zigzag shape as a one long strip
Data flow

## Slide 5
Mechanical Layout
Hangable
Foldable
Portable

## Slide 6
Power Consumption and Optimization
B
We applied the following optimizations to reduce power consumption:
  Limited the brightness of the LEDs to 20 out of 255.
  Limited the colors options in the application to 6 specific colors.
With these optimizations we were able to achieve
The power supply used is 5v, 10A.

## Slide 7
Tetris Application
  Developed Tetris game application in Android Studio.
  Application features:
    Opening frame.
    Left, Right, Rotate and Drop buttons.
    Next block review box.
    Score display.
    Web socket connection with the esp32.

## Slide 8
Application Classes
MainActivity:
  Runs game activity and handle web socket connection and data transfer.
OpeningActivity:
  Runs and handle game opening frame.
GameBoardView:
  Runs all game functionality including game board display, updating score, block and cells functionality.
GameBoardState:
  Holds a list of Blocks on board.

## Slide 9
Application Classes
BlockFactory:
  Creates different types of blocks and assign random color to them.
Block:
  Represents a Tetris block and holds a list of cells.
Cell:
  Handles the behavior of the cells of each block.

## Slide 10
Class Diagram

## Slide 11
Start game sequence diagram

## Slide 12
Establishing WebSocket Communication
1) Android App - Establishing the WebSocket Connection:

## Slide 13
Establishing WebSocket Communication
2) ESP32 - Setting Up WebSocket:

## Slide 14
Data Types
There are 3 data types sent from the application:
  (X, Y, 0/1, color)
  “GAMEOVER,” + score
  "TURN_OFF"

## Slide 15
Sending The Data
Periodically Sending Game Board State Data:

## Slide 16
Generating The Game Board State
1) Handling Game Over State:
2) Generating the Current Game Board State:

## Slide 17
Generating The Game Board State
3) Checking for Cells No Longer Occupied:
4) Finalizing and Returning the String:

## Slide 18
Receiving Data
ESP32: Handling WebSocket Events and Commands:

## Slide 19
Translating The Data
Given data (X, Y, 0/1, color), how do we know what LEDs we should turn on/off:
1) split the giving string, save each coordinate in specific variable:
2) Handling the color:

## Slide 20
Translating The Data
3) calculating the LEDs indices we need to turn on/off:

## Slide 21
Translating The Data
3) Example:

## Slide 22
Translating The Data
4) update the LEDs accordingly:

## Slide 23
Handling The Score
1) On full row event increase the score counter by 1:
2) On game over event send through the web socket the gameover message with the current score counter:

## Slide 24
Handling The Score
3) Giving the score received form the app, treat it as 2-digits number:
4) Save the LED’s indices in the vectors depends on the specific digit value:

## Slide 25
Handling The Score
5) Go over the two vectors and light up the corresponding LEDs:

## Slide 26
Handling The Score
The Final Result:

## Slide 27
Detecting Specific LEDs
In order to easily detect the LEDs number for representing strings or numbers on the led matrix we used EXEL:

## Slide 28
Challenges
  We faced multiple challenges along the way:
  Mechanical Part:
    how to hang the LED matrix.
  Hardware:
    To find suitable power supply for our requirements.
  Software:
    To establish successful WebSocket connection.
    To infer the colors correctly.
    To handle the data received correctly and to know what is the best way to send it.
    X,Y,COLOR – DELETE,X,Y

## Slide 29
The Final Result